## Slide 1
Training Convolutional Neural Networks on FPGAs
Kyle Daruwalla (daruwalla@wisc.edu) and Akhil Sundararajan (asudararaja@wisc.edu)
Hardware Design
All numbers are represented in 16-bit fixed point
  1 sign bit, 1 integer bit, 14 fractional bits
Stochastic rounding is used for quantization
Convolution layers are condensed into a series of parallel ”filter units”
Each unit is capable of performing feed-forward pass and backpropagation
Units keep local register files with weights and biases
Goals and Objectives
Train a CNN using TensorFlow on various Amazon EC2 Spot Instances
Design and validate limited precision CNN training hardware for FPGAs
Simulate limited precision CNN algorithm in MATLAB
Measure and compare accuracy and training time for equivalent number of gradient computations
Design Specifications
CNN Structure: CONV -< POOL -< FC
Software baseline implemented in TensorFlow
  Run on Amazon EC2 c2x.large
  Run on Amazon EC2 c8x.large
MATLAB simulation custom built for limited precision
FPGA design targeting Xilinx Artix-7 Series
Introduction and Motivation
CNNs are popular for image classification, speech recognition, and object recognition
CNN training phase is limited by general purpose hardware
  Memory access latency
  Complex arithmetic units
Field-programmable gate arrays (FPGAs) are a platform for designing specialized hardware
Apply traditional hardware design techniques to the CNN training algorithm
Chart: Training Time for 12, 800, 000 Samples
| Total Runtime (min)
TF w/ EC2 (32 cores) | 47
TF w/ EC2 (8 cores) | 49
FPGA @ 10 MHz | 192
FPGA @20 MHz | 96
FPGA @50 MHz | 38
FPGA @ 100 MHz | 19
Results
Limited Precision Convergence
Insert figure
Conclusions and Future Work
CNNs do not fit on current FPGAs (memory constrained)
Hardware controller does not scale well as CNN grows
Need CNNs with smaller weight kernels
Bulk of future work is in partitioning and communicating between FPGAs
Use quantization noise intelligently to make CNN robust